## Slide 1: Module 12: Non Functional Aspects - Dependability Reliable + Safe + Secure + Resilient Software
Note: Performance/ Usability etc. are skipped
Ref: Chapters 10-14 of Sommerville

## Slide 2: Chapter 10 – Dependable systems Chapter 11 – Reliability Engineering Chapter 12 – Safety Engineering Chapter 13 – Security Engineering Chapter 14 – Resilience Engineering

## Slide 3: Dependable Systems - Topics covered
Dependability properties
Sociotechnical systems
Redundancy and diversity
Dependable processes
Formal methods and dependability

## Slide 4: System dependability
For many computer-based systems, the most important system property is the dependability of the system.
The dependability of a system reflects the user’s degree of trust in that system. It reflects the extent of the user’s confidence that it will operate as users expect and that it will not ‘fail’ in normal use.
Dependability covers the related systems attributes of reliability, availability and security. These are all inter-dependent.

## Slide 5: Importance of dependability
System failures may have widespread effects with large numbers of people affected by the failure.
Systems that are not dependable and are unreliable, unsafe or insecure may be rejected by their users.
The costs of system failure may be very high if the failure leads to economic losses or physical damage.
Undependable systems may cause information loss with a high consequent recovery cost.

## Slide 6: Causes of failure
Hardware failure
  Hardware fails because of design and manufacturing errors or because components have reached the end of their natural life.
Software failure
  Software fails due to errors in its specification, design or implementation.
Operational failure
  Human operators make mistakes. Now perhaps the largest single cause of system failures in socio-technical systems.

## Slide 7: Dependability properties

## Slide 8: The principal dependability properties

## Slide 9: Principal properties
Availability
  The probability that the system will be up and running and able to deliver useful services to users.
Reliability
  The probability that the system will correctly deliver services as expected by users.
Safety
  A judgment of how likely it is that the system will cause damage to people or its environment.

## Slide 10: Principal properties
Security
  A judgment of how likely it is that the system can resist accidental or deliberate intrusions.
Resilience
  A judgment of how well a system can maintain the continuity of its critical services in the presence of disruptive events such as equipment failure and cyberattacks.

## Slide 11: Other dependability properties
Repairability
  Reflects the extent to which the system can be repaired in the event of a failure
Maintainability
  Reflects the extent to which the system can be adapted to new requirements;
Error tolerance
  Reflects the extent to which user input errors can be avoided and tolerated.

## Slide 12: Dependability attribute dependencies
Safe system operation depends on the system being available and operating reliably.
A system may be unreliable because its data has been corrupted by an external attack.
Denial of service attacks on a system are intended to make it unavailable.
If a system is infected with a virus, you cannot be confident in its reliability or safety.

## Slide 13: Dependability achievement
Avoid the introduction of accidental errors when developing the system.
Design V & V processes that are effective in discovering residual errors in the system.
Design systems to be fault tolerant so that they can continue in operation when faults occur
Design protection mechanisms that guard against external attacks.

## Slide 14: Dependability achievement
Configure the system correctly for its operating environment.
Include system capabilities to recognise and resist cyberattacks.
Include recovery mechanisms to help restore normal system service after a failure.

## Slide 15: Dependability costs
Dependability costs tend to increase exponentially as increasing levels of dependability are required.
There are two reasons for this
  The use of more expensive development techniques and hardware that are required to achieve the higher levels of dependability.
  The increased testing and system validation that is required to convince the system client and regulators that the required levels of dependability have been achieved.

## Slide 16: Cost/dependability curve

## Slide 17: Dependability economics
Because of very high costs of dependability achievement, it may be more cost effective to accept untrustworthy systems and pay for failure costs
However, this depends on social and political factors. A reputation for products that can’t be trusted may lose future business
Depends on system type - for business systems in particular, modest levels of dependability may be adequate

## Slide 18: Sociotechnical systems

## Slide 19: Systems and software
Software engineering is not an isolated activity but is part of a broader systems engineering process.
Software systems are therefore not isolated systems but are essential components of broader systems that have a human, social or organizational purpose.
Example
  The wilderness weather system is part of broader weather recording and forecasting systems
  These include hardware and software, forecasting processes, system users, the organizations that depend on weather forecasts, etc.

## Slide 20: The sociotechnical systems stack

## Slide 21: Layers in the STS stack
Equipment
  Hardware devices, some of which may be computers. Most devices will include an embedded system of some kind.
Operating system
  Provides a set of common facilities for higher levels in the system.
Communications and data management
  Middleware that provides access to remote systems and databases.
Application systems
  Specific functionality to meet some organization requirements.

## Slide 22: Layers in the STS stack
Business processes
  A set of processes involving people and computer systems that support the activities of the business.
Organizations
  Higher level strategic business activities that affect the operation of the system.
Society
  Laws, regulation and culture that affect the operation of the system.

## Slide 23: Holistic system design
There are interactions and dependencies between the layers in a system and changes at one level ripple through the other levels
  Example: Change in regulations (society) leads to changes in business processes and application software.
For dependability, a systems perspective is essential
  Contain software failures within the enclosing layers of the STS stack.
  Understand how faults and failures in adjacent layers may affect the software in a system.

## Slide 24: Regulation and compliance
The general model of economic organization that is now almost universal in the world is that privately owned companies offer goods and services and make a profit on these.
To ensure the safety of their citizens, most governments regulate (limit the freedom of) privately owned companies so that they must follow certain standards to ensure that their products are safe and secure.

## Slide 25: Regulated systems
Many critical systems are regulated systems, which means that their use must be approved by an external regulator before the systems go into service.
  Nuclear systems
  Air traffic control systems
  Medical devices
A safety and dependability case has to be approved by the regulator. Therefore, critical systems development has to create the evidence to convince a regulator that the system is dependable, safe and secure.

## Slide 26: Safety regulation
Regulation and compliance (following the rules) applies to the sociotechnical system as a whole and not simply the software element of that system.
Safety-related systems may have to be certified as safe by the regulator.
To achieve certification, companies that are developing safety-critical systems have to produce an extensive safety case that shows that rules and regulations have been followed.
It can be as expensive develop the documentation for certification as it is to develop the system itself.

## Slide 27: Redundancy and diversity

## Slide 28: Redundancy and diversity
Redundancy
  Keep more than a single version of critical components so that if one fails then a backup is available.
Diversity
  Provide the same functionality in different ways in different components so that they will not fail in the same way.
Redundant and diverse components should be independent so that they will not suffer from ‘common-mode’ failures
  For example, components implemented in different programming languages means that a compiler fault will not affect all of them.

## Slide 29: Diversity and redundancy examples
Redundancy. Where availability is critical (e.g. in e-commerce systems), companies normally keep backup servers and switch to these automatically if failure occurs.
Diversity. To provide resilience against external attacks, different servers may be implemented using different operating systems (e.g. Windows and Linux)

## Slide 30: Process diversity and redundancy
Process activities, such as validation, should not depend on a single approach, such as testing, to validate the system.
Redundant and diverse process activities are important especially for verification and validation.
Multiple, different process activities the complement each other and allow for cross-checking help to avoid process errors, which may lead to errors in the software.

## Slide 31: Problems with redundancy and diversity
Adding diversity and redundancy to a system increases the system complexity.
This can increase the chances of error because of unanticipated interactions and dependencies between the redundant system components.
Some engineers therefore advocate simplicity and extensive V & V as a more effective route to software dependability.
Airbus FCS architecture is redundant/diverse; Boeing 777 FCS architecture has no software diversity

## Slide 32: Dependable processes

## Slide 33: Dependable processes
To ensure a minimal number of software faults, it is important to have a well-defined, repeatable software process.
A well-defined repeatable process is one that does not depend entirely on individual skills; rather can be enacted by different people.
Regulators use information about the process to check if good software engineering practice has been used.
For fault detection, it is clear that the process activities should include significant effort devoted to verification and validation.

## Slide 34: Dependable process characteristics
Explicitly defined
  A process that has a defined process model that is used to drive the software production process. Data must be collected during the process that proves that the development team has followed the process as defined in the process model.
Repeatable
  A process that does not rely on individual interpretation and judgment. The process can be repeated across projects and with different team members, irrespective of who is involved in the development.

## Slide 35: Attributes of dependable processes
Process characteristic | Description
Auditable | The process should be understandable by people apart from process participants, who can check that process standards are being followed and make suggestions for process improvement.
Diverse | The process should include redundant and diverse verification and validation activities.
Documentable | The process should have a defined process model that sets out the activities in the process and the documentation that is to be produced during these activities.
Robust | The process should be able to recover from failures of individual process activities.
Standardized | A comprehensive set of software development standards covering software production and documentation should be available.

## Slide 36: Dependable process activities
Requirements reviews to check that the requirements are, as far as possible, complete and consistent.
Requirements management to ensure that changes to the requirements are controlled and that the impact of proposed requirements changes is understood.
Formal specification, where a mathematical model of the software is created and analyzed.
System modeling, where the software design is explicitly documented as a set of graphical models, and the links between the requirements and these models are documented.

## Slide 37: Dependable process activities
Design and program inspections, where the different descriptions of the system are inspected and checked by different people.
Static analysis, where automated checks are carried out on the source code of the program.
Test planning and management, where a comprehensive set of system tests is designed.
  The testing process has to be carefully managed to demonstrate that these tests provide coverage of the system requirements and have been correctly applied in the testing process.

## Slide 38: Dependable processes and agility
Dependable software often requires certification so both process and product documentation has to be produced.
Up-front requirements analysis is also essential to discover requirements and requirements conflicts that may compromise the safety and security of the system.
These conflict with the general approach in agile development of co-development of the requirements and the system and minimizing documentation.

## Slide 39: Dependable processes and agility
An agile process may be defined that incorporates techniques such as iterative development, test-first development and user involvement in the development team.
So long as the team follows that process and documents their actions, agile methods can be used.
However, additional documentation and planning is essential so ‘pure agile’ is impractical for dependable systems engineering.

## Slide 40: Formal methods and dependability

## Slide 41: Formal specification
Formal methods are approaches to software development that are based on mathematical representation and analysis of software.
Formal methods include
  Formal specification;
  Specification analysis and proof;
  Transformational development;
  Program verification.
Formal methods significantly reduce some types of programming errors and can be cost-effective for dependable systems engineering.

## Slide 42: Formal approaches
Verification-based approaches
  Different representations of a software system such as a specification and a program implementing that specification are proved to be equivalent.
  This demonstrates the absence of implementation errors.
Refinement-based approaches
  A representation of a system is systematically transformed into another, lower-level represention e.g. a specification is transformed automatically into an implementation.
  This means that, if the transformation is correct, the representations are equivalent.

## Slide 43: Use of formal methods
The principal benefits of formal methods are in reducing the number of faults in systems.
Consequently, their main area of applicability is in dependable systems engineering. There have been several successful projects where formal methods have been used in this area.
In this area, the use of formal methods is most likely to be cost-effective because high system failure costs must be avoided.

## Slide 44: Classes of error
Specification and design errors and omissions.
  Developing and analysing a formal model of the software may reveal errors and omissions in the software requirements. If the model is generated automatically or systematically from source code, analysis using model checking can find undesirable states that may occur such as deadlock in a concurrent system.
Inconsistences between a specification and a program.
  If a refinement method is used, mistakes made by developers that make the software inconsistent with the specification are avoided. Program proving discovers inconsistencies between a program and its specification.

## Slide 45: Benefits of formal specification
Developing a formal specification requires the system requirements to be analyzed in detail. This helps to detect problems, inconsistencies and incompleteness in the requirements.
As the specification is expressed in a formal language, it can be automatically analyzed to discover inconsistencies and incompleteness.
If you use a formal method such as the B method, you can transform the formal specification into a ‘correct’ program.
Program testing costs may be reduced if the program is formally verified against its specification.

## Slide 46: Acceptance of formal methods
Formal methods have had limited impact on practical software development:
  Problem owners cannot understand a formal specification and so cannot assess if it is an accurate representation of their requirements.
  It is easy to assess the costs of developing a formal specification but harder to assess the benefits. Managers may therefore be unwilling to invest in formal methods.
  Software engineers are unfamiliar with this approach and are therefore reluctant to propose the use of FM.
  Formal methods are still hard to scale up to large systems.
  Formal specification is not really compatible with agile development methods.

## Slide 47: Key points
System dependability is important because failure of critical systems can lead to economic losses, information loss, physical damage or threats to human life.
The dependability of a computer system is a system property that reflects the user’s degree of trust in the system. The most important dimensions of dependability are availability, reliability, safety, security and resilience.
Sociotechnical systems include computer hardware, software and people, and are situated within an organization. They are designed to support organizational or business goals and objectives.

## Slide 48: Key points
The use of a dependable, repeatable process is essential if faults in a system are to be minimized. The process should include verification and validation activities at all stages, from requirements definition through to system implementation.
The use of redundancy and diversity in hardware, software processes and software systems is essential to the development of dependable systems.
Formal methods, where a formal model of a system is used as a basis for development help reduce the number of specification and implementation errors in a system.

## Slide 49: Chapter 11 – Reliability Engineering

## Slide 50: Topics covered
Availability and reliability
Reliability requirements
Fault-tolerant architectures
Programming for reliability
Reliability measurement

## Slide 51: Software reliability
In general, software customers expect all software to be dependable. However, for non-critical applications, they may be willing to accept some system failures.
Some applications (critical systems) have very high reliability requirements and special software engineering techniques may be used to achieve this.
  Medical systems
  Telecommunications and power systems
  Aerospace systems

## Slide 52: Faults, errors and failures
Term | Description
Human error or mistake | Human behavior that results in the introduction of faults into a system. For example, in the wilderness weather system, a programmer might decide that the way to compute the time for the next transmission is to add 1 hour to the current time. This works except when the transmission time is between 23.00 and midnight (midnight is 00.00 in the 24-hour clock).
System fault | A characteristic of a software system that can lead to a system error. The fault is the inclusion of the code to add 1 hour to the time of the last transmission, without a check if the time is greater than or equal to 23.00.
System error | An erroneous system state that can lead to system behavior that is unexpected by system users. The value of transmission time is set incorrectly (to 24.XX rather than 00.XX) when the faulty code is executed.
System failure | An event that occurs at some point in time when the system does not deliver a service as expected by its users. No weather data is transmitted because the time is invalid.

## Slide 53: Faults and failures
Failures are a usually a result of system errors that are derived from faults in the system
However, faults do not necessarily result in system errors
  The erroneous system state resulting from the fault may be transient and ‘corrected’ before an error arises.
  The faulty code may never be executed.
Errors do not necessarily lead to system failures
  The error can be corrected by built-in error detection and recovery
  The failure can be protected against by built-in protection facilities. These may, for example, protect system resources from system errors

## Slide 54: Fault management
Fault avoidance
  The system is developed in such a way that human error is avoided and thus system faults are minimised.
  The development process is organised so that faults in the system are detected and repaired before delivery to the customer.
Fault detection
  Verification and validation techniques are used to discover and remove faults in a system before it is deployed.
Fault tolerance
  The system is designed so that faults in the delivered software do not result in system failure.

## Slide 55: Reliability achievement
Fault avoidance
  Development technique are used that either minimise the possibility of mistakes or trap mistakes before they result in the introduction of system faults.
Fault detection and removal
  Verification and validation techniques are used that increase the probability of detecting and correcting errors before the system goes into service are used.
Fault tolerance
  Run-time techniques are used to ensure that system faults do not result in system errors and/or that system errors do not lead to system failures.

## Slide 56: The increasing costs of residual fault removal

## Slide 57: Availability and reliability

## Slide 58: Availability and reliability
Reliability
  The probability of failure-free system operation over a specified time in a given environment for a given purpose
Availability
  The probability that a system, at a point in time, will be operational and able to deliver the requested services
Both of these attributes can be expressed quantitatively e.g. availability of 0.999 means that the system is up and running for 99.9% of the time.

## Slide 59: Reliability and specifications
Reliability can only be defined formally with respect to a system specification i.e. a failure is a deviation from a specification.
However, many specifications are incomplete or incorrect – hence, a system that conforms to its specification may ‘fail’ from the perspective of system users.
Furthermore, users don’t read specifications so don’t know how the system is supposed to behave.
Therefore perceived reliability is more important in practice.

## Slide 60: Perceptions of reliability
The formal definition of reliability does not always reflect the user’s perception of a system’s reliability
  The assumptions that are made about the environment where a system will be used may be incorrect
    Usage of a system in an office environment is likely to be quite different from usage of the same system in a university environment
  The consequences of system failures affects the perception of reliability
    Unreliable windscreen wipers in a car may be irrelevant in a dry climate
    Failures that have serious consequences (such as an engine breakdown in a car) are given greater weight by users than failures that are inconvenient

## Slide 61: A system as an input/output mapping

## Slide 62: Availability perception
Availability is usually expressed as a percentage of the time that the system is available to deliver services e.g. 99.95%.
However, this does not take into account two factors:
  The number of users affected by the service outage. Loss of service in the middle of the night is less important for many systems than loss of service during peak usage periods.
  The length of the outage. The longer the outage, the more the disruption. Several short outages are less likely to be disruptive than 1 long outage. Long repair times are a particular problem.

## Slide 63: Software usage patterns

## Slide 64: Reliability in use
Removing X% of the faults in a system will not necessarily improve the reliability by X%.
Program defects may be in rarely executed sections of the code so may never be encountered by users. Removing these does not affect the perceived reliability.
Users adapt their behaviour to avoid system features that may fail for them.
A program with known faults may therefore still be perceived as reliable by its users.

## Slide 65: Reliability requirements

## Slide 66: System reliability requirements
Functional reliability requirements define system and software functions that avoid, detect or tolerate faults in the software and so ensure that these faults do not lead to system failure.
Software reliability requirements may also be included to cope with hardware failure or operator error.
  Reliability is a measurable system attribute so non-functional reliability requirements may be specified quantitatively. These define the number of failures that are acceptable during normal use of the system or the time in which the system must be available.

## Slide 67: Reliability metrics
Reliability metrics are units of measurement of system reliability.
System reliability is measured by counting the number of operational failures and, where appropriate, relating these to the demands made on the system and the time that the system has been operational.
A long-term measurement programme is required to assess the reliability of critical systems.
Metrics
  Probability of failure on demand
  Rate of occurrence of failures/Mean time to failure
  Availability

## Slide 68: Probability of failure on demand (POFOD)
This is the probability that the system will fail when a service request is made. Useful when demands for service are intermittent and relatively infrequent.
Appropriate for protection systems where services are demanded occasionally and where there are serious consequence if the service is not delivered.
Relevant for many safety-critical systems with exception management components
  Emergency shutdown system in a chemical plant.

## Slide 69: Rate of fault occurrence (ROCOF)
Reflects the rate of occurrence of failure in the system.
ROCOF of 0.002 means 2 failures are likely in each 1000 operational time units e.g. 2 failures per 1000 hours of operation.
Relevant for systems where the system has to process a large number of similar requests in a short time
  Credit card processing system, airline booking system.
Reciprocal of ROCOF is Mean time to Failure (MTTF)
  Relevant for systems with long transactions i.e. where system processing takes a long time (e.g. CAD systems). MTTF should be longer than expected transaction length.

## Slide 70: Availability
Measure of the fraction of the time that the system is available for use.
Takes repair and restart time into account
Availability of 0.998 means software is available for 998 out of 1000 time units.
Relevant for non-stop, continuously running systems
  telephone switching systems, railway signalling systems.

## Slide 71: Availability specification
Availability | Explanation
0.9 | The system is available for 90% of the time. This means that, in a 24-hour period (1,440 minutes), the system will be unavailable for 144 minutes.
0.99 | In a 24-hour period, the system is unavailable for 14.4 minutes.
0.999 | The system is unavailable for 84 seconds in a 24-hour period.
0.9999 | The system is unavailable for 8.4 seconds in a 24-hour period. Roughly, one minute per week.

## Slide 72: Non-functional reliability requirements
Non-functional reliability requirements are specifications of the required reliability and availability of a system using one of the reliability metrics (POFOD, ROCOF or AVAIL).
Quantitative reliability and availability specification has been used for many years in safety-critical systems but is uncommon for business critical systems.
However, as more and more companies demand 24/7 service from their systems, it makes sense for them to be precise about their reliability and availability expectations.

## Slide 73: Benefits of reliability specification
The process of deciding the required level of the reliability helps to clarify what stakeholders really need.
It provides a basis for assessing when to stop testing a system. You stop when the system has reached its required reliability level.
It is a means of assessing different design strategies intended to improve the reliability of a system.
If a regulator has to approve a system (e.g. all systems that are critical to flight safety on an aircraft are regulated), then evidence that a required reliability target has been met is important for system certification.

## Slide 74: Specifying reliability requirements
Specify the availability and reliability requirements for different types of failure. There should be a lower probability of high-cost failures than failures that don’t have serious consequences.
Specify the availability and reliability requirements for different types of system service. Critical system services should have the highest reliability but you may be willing to tolerate more failures in less critical services.
Think about whether a high level of reliability is really required. Other mechanisms can be used to provide reliable system service.

## Slide 75: ATM reliability specification
Key concerns
  To ensure that their ATMs carry out customer services as requested and that they properly record customer transactions in the account database.
  To ensure that these ATM systems are available for use when required.
Database transaction mechanisms may be used to correct transaction problems so a low-level of ATM reliability is all that is required
Availability, in this case, is more important than reliability

## Slide 76: ATM availability specification
System services
  The customer account database service;
  The individual services provided by an ATM such as ‘withdraw cash’, ‘provide account information’, etc.
The database service is critical as failure of this service means that all of the ATMs in the network are out of action.
You should specify this to have a high level of availability.
  Database availability should be around 0.9999, between 7 am and 11pm.
  This corresponds to a downtime of less than 1 minute per week.

## Slide 77: ATM availability specification
For an individual ATM, the key reliability issues depends on mechanical reliability and the fact that it can run out of cash.
A lower level of software availability for the ATM software is acceptable.
The overall availability of the ATM software might therefore be specified as 0.999, which means that a machine might be unavailable for between 1 and 2 minutes each day.

## Slide 78: Insulin pump reliability specification
Probability of failure (POFOD) is the most appropriate metric.
Transient failures that can be repaired by user actions such as recalibration of the machine. A relatively low value of POFOD is acceptable (say 0.002) – one failure may occur in every 500 demands.
Permanent failures require the software to be re-installed by the manufacturer. This should occur no more than once per year. POFOD for this situation should be less than 0.00002.

## Slide 79: Functional reliability requirements
Checking requirements that identify checks to ensure that incorrect data is detected before it leads to a failure.
Recovery requirements that are geared to help the system recover after a failure has occurred.
Redundancy requirements that specify redundant features of the system to be included.
Process requirements for reliability which specify the development process to be used may also be included.

## Slide 80: Examples of functional reliability requirements
RR1: A pre-defined range for all operator inputs shall be defined and the system shall check that all operator inputs fall within this pre-defined range. (Checking)
RR2: Copies of the patient database shall be maintained on two separate servers that are not housed in the same building. (Recovery, redundancy)
RR3: N-version programming shall be used to implement the braking control system. (Redundancy)
RR4: The system must be implemented in a safe subset of Ada and checked using static analysis. (Process)

## Slide 81: Fault-tolerant architectures

## Slide 82: Fault tolerance
In critical situations, software systems must be fault tolerant.
Fault tolerance is required where there are high availability requirements or where system failure costs are very high.
Fault tolerance means that the system can continue in operation in spite of software failure.
Even if the system has been proved to conform to its specification, it must also be fault tolerant as there may be specification errors or the validation may be incorrect.

## Slide 83: Fault-tolerant system architectures
Fault-tolerant systems architectures are used in situations where fault tolerance is essential. These architectures are generally all based on redundancy and diversity.
Examples of situations where dependable architectures are used:
  Flight control systems, where system failure could threaten the safety of passengers
  Reactor systems where failure of a control system could lead to a chemical or nuclear emergency
  Telecommunication systems, where there is a need for 24/7 availability.

## Slide 84: Protection systems
A specialized system that is associated with some other control system, which can take emergency action if a failure occurs.
  System to stop a train if it passes a red light
  System to shut down a reactor if temperature/pressure are too high
Protection systems independently monitor the controlled system and the environment.
If a problem is detected, it issues commands to take emergency action to shut down the system and avoid a catastrophe.

## Slide 85: Protection system architecture

## Slide 86: Protection system functionality
Protection systems are redundant because they include monitoring and control capabilities that replicate those in the control software.
Protection systems should be diverse and use different technology from the control software.
They are simpler than the control system so more effort can be expended in validation and dependability assurance.
Aim is to ensure that there is a low probability of failure on demand for the protection system.

## Slide 87: Self-monitoring architectures
Multi-channel architectures where the system monitors its own operations and takes action if inconsistencies are detected.
The same computation is carried out on each channel and the results are compared. If the results are identical and are produced at the same time, then it is assumed that the system is operating correctly.
If the results are different, then a failure is assumed and a failure exception is raised.

## Slide 88: Self-monitoring architecture

## Slide 89: Self-monitoring systems
Hardware in each channel has to be diverse so that common mode hardware failure will not lead to each channel producing the same results.
Software in each channel must also be diverse, otherwise the same software error would affect each channel.
If high-availability is required, you may use several self-checking systems in parallel.
  This is the approach used in the Airbus family of aircraft for their flight control systems.

## Slide 90: Airbus flight control system architecture

## Slide 91: Airbus architecture discussion
The Airbus FCS has 5 separate computers, any one of which can run the control software.
Extensive use has been made of diversity
  Primary systems use a different processor from the secondary systems.
  Primary and secondary systems use chipsets from different manufacturers.
  Software in secondary systems is less complex than in primary system – provides only critical functionality.
  Software in each channel is developed in different programming languages by different teams.
  Different programming languages used in primary and secondary systems.

## Slide 92: N-version programming
Multiple versions of a software system carry out computations at the same time. There should be an odd number of computers involved, typically 3.
The results are compared using a voting system and the majority result is taken to be the correct result.
Approach derived from the notion of triple-modular redundancy, as used in hardware systems.

## Slide 93: Hardware fault tolerance
Depends on triple-modular redundancy (TMR).
There are three replicated identical components that receive the same input and whose outputs are compared.
If one output is different, it is ignored and component failure is assumed.
Based on most faults resulting from component failures rather than design faults and a low probability of simultaneous component failure.

## Slide 94: Triple modular redundancy

## Slide 95: N-version programming

## Slide 96: N-version programming
The different system versions are designed and implemented by different teams. It is assumed that there is a low probability that they will make the same mistakes. The algorithms used should but may not be different.
There is some empirical evidence that teams commonly misinterpret specifications in the same way and chose the same algorithms in their systems.

## Slide 97: Software diversity
Approaches to software fault tolerance depend on software diversity where it is assumed that different implementations of the same software specification will fail in different ways.
It is assumed that implementations are (a) independent and (b) do not include common errors.
Strategies to achieve diversity
  Different programming languages
  Different design methods and tools
  Explicit specification of different algorithms

## Slide 98: Problems with design diversity
Teams are not culturally diverse so they tend to tackle problems in the same way.
Characteristic errors
  Different teams make the same mistakes. Some parts of an implementation are more difficult than others so all teams tend to make mistakes in the same place;
  Specification errors;
  If there is an error in the specification then this is reflected in all implementations;
  This can be addressed to some extent by using multiple specification representations.

## Slide 99: Specification dependency
Both approaches to software redundancy are susceptible to specification errors. If the specification is incorrect, the system could fail
This is also a problem with hardware but software specifications are usually more complex than hardware specifications and harder to validate.
This has been addressed in some cases by developing separate software specifications from the same user specification.

## Slide 100: Improvements in practice
In principle, if diversity and independence can be achieved, multi-version programming leads to very significant improvements in reliability and availability.
In practice, observed improvements are much less significant but the approach seems leads to reliability improvements of between 5 and 9 times.
The key question is whether or not such improvements are worth the considerable extra development costs for multi-version programming.

## Slide 101: Programming for reliability

## Slide 102: Dependable programming
Good programming practices can be adopted that help reduce the incidence of program faults.
These programming practices support
  Fault avoidance
  Fault detection
  Fault tolerance

## Slide 103: Good practice guidelines for dependable programming
Dependable programming guidelines 1. Limit the visibility of information in a program 2. Check all inputs for validity 3. Provide a handler for all exceptions 4. Minimize the use of error-prone constructs 5. Provide restart capabilities 6. Check array bounds 7. Include timeouts when calling external components 8. Name all constants that represent real-world values | 

## Slide 104: (1) Limit the visibility of information in a program
Program components should only be allowed access to data that they need for their implementation.
This means that accidental corruption of parts of the program state by these components is impossible.
You can control visibility by using abstract data types where the data representation is private and you only allow access to the data through predefined operations such as get () and put ().

## Slide 105: (2) Check all inputs for validity
All program take inputs from their environment and make assumptions about these inputs.
However, program specifications rarely define what to do if an input is not consistent with these assumptions.
Consequently, many programs behave unpredictably when presented with unusual inputs and, sometimes, these are threats to the security of the system.
Consequently, you should always check inputs before processing against the assumptions made about these inputs.

## Slide 106: Validity checks
Range checks
  Check that the input falls within a known range.
Size checks
  Check that the input does not exceed some maximum size e.g. 40 characters for a name.
Representation checks
  Check that the input does not include characters that should not be part of its representation e.g. names do not include numerals.
Reasonableness checks
  Use information about the input to check if it is reasonable rather than an extreme value.

## Slide 107: (3) Provide a handler for all exceptions
A program exception is an error or some unexpected event such as a power failure.
Exception handling constructs allow for such events to be handled without the need for continual status checking to detect exceptions.
Using normal control constructs to detect exceptions needs many additional statements to be added to the program. This adds a significant overhead and is potentially error-prone.

## Slide 108: Exception handling

## Slide 109: Exception handling
Three possible exception handling strategies
  Signal to a calling component that an exception has occurred and provide information about the type of exception.
  Carry out some alternative processing to the processing where the exception occurred. This is only possible where the exception handler has enough information to recover from the problem that has arisen.
  Pass control to a run-time support system to handle the exception.
Exception handling is a mechanism to provide some fault tolerance

## Slide 110: (4) Minimize the use of error-prone constructs
Program faults are usually a consequence of human error because programmers lose track of the relationships between the different parts of the system
This is exacerbated by error-prone constructs in programming languages that are inherently complex or that don’t check for mistakes when they could do so.
Therefore, when programming, you should try to avoid or at least minimize the use of these error-prone constructs.

## Slide 111: Error-prone constructs
Unconditional branch (goto) statements
Floating-point numbers
  Inherently imprecise. The imprecision may lead to invalid comparisons.
Pointers
  Pointers referring to the wrong memory areas can corrupt data. Aliasing can make programs difficult to understand and change.
Dynamic memory allocation
  Run-time allocation can cause memory overflow.

## Slide 112: Error-prone constructs
Parallelism
  Can result in subtle timing errors because of unforeseen interaction between parallel processes.
Recursion
  Errors in recursion can cause memory overflow as the program stack fills up.
Interrupts
  Interrupts can cause a critical operation to be terminated and make a program difficult to understand.
Inheritance
  Code is not localised. This can result in unexpected behaviour when changes are made and problems of understanding the code.

## Slide 113: Error-prone constructs
Aliasing
  Using more than 1 name to refer to the same state variable.
Unbounded arrays
  Buffer overflow failures can occur if no bound checking on arrays.
Default input processing
  An input action that occurs irrespective of the input.
  This can cause problems if the default action is to transfer control elsewhere in the program. In incorrect or deliberately malicious input can then trigger a program failure.

## Slide 114: (5) Provide restart capabilities
For systems that involve long transactions or user interactions, you should always provide a restart capability that allows the system to restart after failure without users having to redo everything that they have done.
Restart depends on the type of system
  Keep copies of forms so that users don’t have to fill them in again if there is a problem
  Save state periodically and restart from the saved state

## Slide 115: (6) Check array bounds
In some programming languages, such as C, it is possible to address a memory location outside of the range allowed for in an array declaration.
This leads to the well-known ‘bounded buffer’ vulnerability where attackers write executable code into memory by deliberately writing beyond the top element in an array.
If your language does not include bound checking, you should therefore always check that an array access is within the bounds of the array.

## Slide 116: (7) Include timeouts when calling external components
In a distributed system, failure of a remote computer can be ‘silent’ so that programs expecting a service from that computer may never receive that service or any indication that there has been a failure.
To avoid this, you should always include timeouts on all calls to external components.
After a defined time period has elapsed without a response, your system should then assume failure and take whatever actions are required to recover from this.

## Slide 117: (8) Name all constants that represent real-world values
Always give constants that reflect real-world values (such as tax rates) names rather than using their numeric values and always refer to them by name
You are less likely to make mistakes and type the wrong value when you are using a name rather than a value.
This means that when these ‘constants’ change (for sure, they are not really constant), then you only have to make the change in one place in your program.

## Slide 118: Reliability measurement

## Slide 119: Reliability measurement
To assess the reliability of a system, you have to collect data about its operation. The data required may include:
  The number of system failures given a number of requests for system services. This is used to measure the POFOD. This applies irrespective of the time over which the demands are made.
  The time or the number of transactions between system failures plus the total elapsed time or total number of transactions. This is used to measure ROCOF and MTTF.
  The repair or restart time after a system failure that leads to loss of service. This is used in the measurement of availability. Availability does not just depend on the time between failures but also on the time required to get the system back into operation.

## Slide 120: Reliability testing
Reliability testing (Statistical testing) involves running the program to assess whether or not it has reached the required level of reliability.
This cannot normally be included as part of a normal defect testing process because data for defect testing is (usually) atypical of actual usage data.
Reliability measurement therefore requires a specially designed data set that replicates the pattern of inputs to be processed by the system.

## Slide 121: Statistical testing
Testing software for reliability rather than fault detection.
Measuring the number of errors allows the reliability of the software to be predicted. Note that, for statistical reasons, more errors than are allowed for in the reliability specification must be induced.
An acceptable level of reliability should be specified and the software tested and amended until that level of reliability is reached.

## Slide 122: Reliability measurement

## Slide 123: Reliability measurement problems
Operational profile uncertainty
  The operational profile may not be an accurate reflection of the real use of the system.
High costs of test data generation
  Costs can be very high if the test data for the system cannot be generated automatically.
Statistical uncertainty
  You need a statistically significant number of failures to compute the reliability but highly reliable systems will rarely fail.
Recognizing failure
  It is not always obvious when a failure has occurred as there may be conflicting interpretations of a specification.

## Slide 124: Operational profiles
An operational profile is a set of test data whose frequency matches the actual frequency of these inputs from ‘normal’ usage of the system. A close match with actual usage is necessary otherwise the measured reliability will not be reflected in the actual usage of the system.
It can be generated from real data collected from an existing system or (more often) depends on assumptions made about the pattern of usage of a system.

## Slide 125: An operational profile

## Slide 126: Operational profile generation
Should be generated automatically whenever possible.
Automatic profile generation is difficult for interactive systems.
May be straightforward for ‘normal’ inputs but it is difficult to predict ‘unlikely’ inputs and to create test data for them.
Pattern of usage of new systems is unknown.
Operational profiles are not static but change as users learn about a new system and change the way that they use it.

## Slide 127: Key points
Software reliability can be achieved by avoiding the introduction of faults, by detecting and removing faults before system deployment and by including fault tolerance facilities that allow the system to remain operational after a fault has caused a system failure.
Reliability requirements can be defined quantitatively in the system requirements specification.
Reliability metrics include probability of failure on demand (POFOD), rate of occurrence of failure (ROCOF) and availability (AVAIL).

## Slide 128: Key points
Functional reliability requirements are requirements for system functionality, such as checking and redundancy requirements, which help the system meet its non-functional reliability requirements.
Dependable system architectures are system architectures that are designed for fault tolerance.
There are a number of architectural styles that support fault tolerance including protection systems, self-monitoring architectures and N-version programming.

## Slide 129: Key points
Software diversity is difficult to achieve because it is practically impossible to ensure that each version of the software is truly independent.
Dependable programming relies on including redundancy in a program as checks on the validity of inputs and the values of program variables.
Statistical testing is used to estimate software reliability. It relies on testing the system with test data that matches an operational profile, which reflects the distribution of inputs to the software when it is in use.

## Slide 130: Chapter 12 – Safety Engineering

## Slide 131: Topics covered
Safety-critical systems
Safety requirements
Safety engineering processes
Safety cases

## Slide 132: Safety
Safety is a property of a system that reflects the system’s ability to operate, normally or abnormally, without danger of causing human injury or death and without damage to the system’s environment.
It is important to consider software safety as most devices whose failure is critical now incorporate software-based control systems.

## Slide 133: Software in safety-critical systems
The system may be software-controlled so that the decisions made by the software and subsequent actions are safety-critical. Therefore, the software behaviour is directly related to the overall safety of the system.
Software is extensively used for checking and monitoring other safety-critical components in a system. For example, all aircraft engine components are monitored by software looking for early indications of component failure. This software is safety-critical because, if it fails, other components may fail and cause an accident.

## Slide 134: Safety and reliability
Safety and reliability are related but distinct
  In general, reliability and availability are necessary but not sufficient conditions for system safety
Reliability is concerned with conformance to a given specification and delivery of service
Safety is concerned with ensuring system cannot cause damage irrespective of whether or not it conforms to its specification.
  System reliability is essential for safety but is not enough
  Reliable systems can be unsafe

## Slide 135: Unsafe reliable systems
There may be dormant faults in a system that are undetected for many years and only rarely arise.
Specification errors
  If the system specification is incorrect then the system can behave as specified but still cause an accident.
Hardware failures generating spurious inputs
  Hard to anticipate in the specification.
Context-sensitive commands i.e. issuing the right command at the wrong time
  Often the result of operator error.

## Slide 136: Safety-critical systems

## Slide 137: Safety critical systems
Systems where it is essential that system operation is always safe i.e. the system should never cause damage to people or the system’s environment
Examples
  Control and monitoring systems in aircraft
  Process control systems in chemical manufacture
  Automobile control systems such as braking and engine management systems

## Slide 138: Safety criticality
Primary safety-critical systems
  Embedded software systems whose failure can cause the associated hardware to fail and directly threaten people. Example is the insulin pump control system.
Secondary safety-critical systems
  Systems whose failure results in faults in other (socio-technical) systems, which can then have safety consequences.
    For example, the Mentcare system is safety-critical as failure may lead to inappropriate treatment being prescribed.
    Infrastructure control systems are also secondary safety-critical systems.

## Slide 139: Hazards
Situations or events that can lead to an accident
  Stuck valve in reactor control system
  Incorrect computation by software in navigation system
  Failure to detect possible allergy in medication prescribing system
Hazards do not inevitably result in accidents – accident prevention actions can be taken.

## Slide 140: Safety achievement
Hazard avoidance
  The system is designed so that some classes of hazard simply cannot arise.
Hazard detection and removal
  The system is designed so that hazards are detected and removed before they result in an accident.
Damage limitation
  The system includes protection features that minimise the damage that may result from an accident.

## Slide 141: Safety terminology
Term | Definition
Accident (or mishap) | An unplanned event or sequence of events which results in human death or injury, damage to property, or to the environment. An overdose of insulin is an example of an accident.
Hazard | A condition with the potential for causing or contributing to an accident. A failure of the sensor that measures blood glucose is an example of a hazard.
Damage | A measure of the loss resulting from a mishap. Damage can range from many people being killed as a result of an accident to minor injury or property damage. Damage resulting from an overdose of insulin could be serious injury or the death of the user of the insulin pump.
Hazard severity | An assessment of the worst possible damage that could result from a particular hazard. Hazard severity can range from catastrophic, where many people are killed, to minor, where only minor damage results. When an individual death is a possibility, a reasonable assessment of hazard severity is ‘very high’.
Hazard probability | The probability of the events occurring which create a hazard. Probability values tend to be arbitrary but range from ‘probable’ (say 1/100 chance of a hazard occurring) to ‘implausible’ (no conceivable situations are likely in which the hazard could occur). The probability of a sensor failure in the insulin pump that results in an overdose is probably low.
Risk | This is a measure of the probability that the system will cause an accident. The risk is assessed by considering the hazard probability, the hazard severity, and the probability that the hazard will lead to an accident. The risk of an insulin overdose is probably medium to low.

## Slide 142: Normal accidents
Accidents in complex systems rarely have a single cause as these systems are designed to be resilient to a single point of failure
  Designing systems so that a single point of failure does not cause an accident is a fundamental principle of safe systems design.
Almost all accidents are a result of combinations of malfunctions rather than single failures.
It is probably the case that anticipating all problem combinations, especially, in software controlled systems is impossible so achieving complete safety is impossible. Accidents are inevitable.

## Slide 143: Software safety benefits
Although software failures can be safety-critical, the use of software control systems contributes to increased system safety
  Software monitoring and control allows a wider range of conditions to be monitored and controlled than is possible using electro-mechanical safety systems.
  Software control allows safety strategies to be adopted that reduce the amount of time people spend in hazardous environments.
  Software can detect and correct safety-critical operator errors.

## Slide 144: Safety requirements

## Slide 145: Safety specification
The goal of safety requirements engineering is to identify protection requirements that ensure that system failures do not cause injury or death or environmental damage.
Safety requirements may be ‘shall not’ requirements i.e. they define situations and events that should never occur.
Functional safety requirements define:
  Checking and recovery features that should be included in a system
  Features that provide protection against system failures and external attacks

## Slide 146: Hazard-driven analysis
Hazard identification
Hazard assessment
Hazard analysis
Safety requirements specification

## Slide 147: Hazard identification
Identify the hazards that may threaten the system.
Hazard identification may be based on different types of hazard:
  Physical hazards
  Electrical hazards
  Biological hazards
  Service failure hazards
  Etc.

## Slide 148: Insulin pump risks
Insulin overdose (service failure).
Insulin underdose (service failure).
Power failure due to exhausted battery (electrical).
Electrical interference with other medical equipment (electrical).
Poor sensor and actuator contact (physical).
Parts of machine break off in body (physical).
Infection caused by introduction of machine (biological).
Allergic reaction to materials or insulin (biological).

## Slide 149: Hazard assessment
The process is concerned with understanding the likelihood that a risk will arise and the potential consequences if an accident or incident should occur.
Risks may be categorised as:
  Intolerable. Must never arise or result in an accident
  As low as reasonably practical(ALARP). Must minimise the possibility of risk given cost and schedule constraints
  Acceptable. The consequences of the risk are acceptable and no extra costs should be incurred to reduce hazard probability

## Slide 150: The risk triangle

## Slide 151: Social acceptability of risk
The acceptability of a risk is determined by human, social and political considerations.
In most societies, the boundaries between the regions are pushed upwards with time i.e. society is less willing to accept risk
  For example, the costs of cleaning up pollution may be less than the costs of preventing it but this may not be socially acceptable.
Risk assessment is subjective
  Risks are identified as probable, unlikely, etc. This depends on who is making the assessment.

## Slide 152: Hazard assessment
Estimate the risk probability and the risk severity.
It is not normally possible to do this precisely so relative values are used such as ‘unlikely’, ‘rare’, ‘very high’, etc.
The aim must be to exclude risks that are likely to arise or that have high severity.

## Slide 153: Risk classification for the insulin pump
Identified hazard | Hazard probability | Accident severity | Estimated risk | Acceptability
1.Insulin overdose computation | Medium | High | High | Intolerable
2. Insulin underdose computation | Medium | Low | Low | Acceptable
3. Failure of hardware monitoring system | Medium | Medium | Low | ALARP
4. Power failure | High | Low | Low | Acceptable
5. Machine incorrectly fitted | High | High | High | Intolerable
6. Machine breaks in patient | Low | High | Medium | ALARP
7. Machine causes infection | Medium | Medium | Medium | ALARP
8. Electrical interference | Low | High | Medium | ALARP
9. Allergic reaction | Low | Low | Low | Acceptable

## Slide 154: Hazard analysis
Concerned with discovering the root causes of risks in a particular system.
Techniques have been mostly derived from safety-critical systems and can be
  Inductive, bottom-up techniques. Start with a proposed system failure and assess the hazards that could arise from that failure;
  Deductive, top-down techniques. Start with a hazard and deduce what the causes of this could be.

## Slide 155: Fault-tree analysis
A deductive top-down technique.
Put the risk or hazard at the root of the tree and identify the system states that could lead to that hazard.
Where appropriate, link these with ‘and’ or ‘or’ conditions.
A goal should be to minimise the number of single causes of system failure.

## Slide 156: An example of a software fault tree

## Slide 157: Fault tree analysis
Three possible conditions that can lead to delivery of incorrect dose of insulin
  Incorrect measurement of blood sugar level
  Failure of delivery system
  Dose delivered at wrong time
By analysis of the fault tree, root causes of these hazards related to software are:
  Algorithm error
  Arithmetic error

## Slide 158: Risk reduction
The aim of this process is to identify dependability requirements that specify how the risks should be managed and ensure that accidents/incidents do not arise.
Risk reduction strategies
  Hazard avoidance;
  Hazard detection and removal;
  Damage limitation.

## Slide 159: Strategy use
Normally, in critical systems, a mix of risk reduction strategies are used.
In a chemical plant control system, the system will include sensors to detect and correct excess pressure in the reactor.
However, it will also include an independent protection system that opens a relief valve if dangerously high pressure is detected.

## Slide 160: Insulin pump - software risks
Arithmetic error
  A computation causes the value of a variable to overflow or underflow;
  Maybe include an exception handler for each type of arithmetic error.
Algorithmic error
  Compare dose to be delivered with previous dose or safe maximum doses. Reduce dose if too high.

## Slide 161: Examples of safety requirements
SR1: The system shall not deliver a single dose of insulin that is greater than a specified maximum dose for a system user.
SR2: The system shall not deliver a daily cumulative dose of insulin that is greater than a specified maximum daily dose for a system user.
SR3: The system shall include a hardware diagnostic facility that shall be executed at least four times per hour.
SR4: The system shall include an exception handler for all of the exceptions that are identified in Table 3.
SR5: The audible alarm shall be sounded when any hardware or software anomaly is discovered and a diagnostic message, as defined in Table 4, shall be displayed.
SR6: In the event of an alarm, insulin delivery shall be suspended until the user has reset the system and cleared the alarm.

## Slide 162: Safety engineering processes

## Slide 163: Safety engineering processes
Safety engineering processes are based on reliability engineering processes
  Plan-based approach with reviews and checks at each stage in the process
  General goal of fault avoidance and fault detection
  Must also include safety reviews and explicit identification and tracking of hazards

## Slide 164: Regulation
Regulators may require evidence that safety engineering processes have been used in system development
For example:
  The specification of the system that has been developed and records of the checks made on that specification.
  Evidence of the verification and validation processes that have been carried out and the results of the system verification and validation.
  Evidence that the organizations developing the system have defined and dependable software processes that include safety assurance reviews. There must also be records that show that these processes have been properly enacted.

## Slide 165: Agile methods and safety
Agile methods are not usually used for safety-critical systems engineering
  Extensive process and product documentation is needed for system regulation. Contradicts the focus in agile methods on the software itself.
  A detailed safety analysis of a complete system specification is important. Contradicts the interleaved development of a system specification and program.
Some agile techniques such as test-driven development may be used

## Slide 166: Safety assurance processes
Process assurance involves defining a dependable process and ensuring that this process is followed during the system development.
Process assurance focuses on:
  Do we have the right processes? Are the processes appropriate for the level of dependability required. Should include requirements management, change management, reviews and inspections, etc.
  Are we doing the processes right? Have these processes been followed by the development team.
Process assurance generates documentation
  Agile processes therefore are rarely used for critical systems.

## Slide 167: Processes for safety assurance
Process assurance is important for safety-critical systems development:
  Accidents are rare events so testing may not find all problems;
  Safety requirements are sometimes ‘shall not’ requirements so cannot be demonstrated through testing.
Safety assurance activities may be included in the software process that record the analyses that have been carried out and the people responsible for these.
  Personal responsibility is important as system failures may lead to subsequent legal actions.

## Slide 168: Safety related process activities
Creation of a hazard logging and monitoring system.
Appointment of project safety engineers who have explicit responsibility for system safety.
Extensive use of safety reviews.
Creation of a safety certification system where the safety of critical components is formally certified.
Detailed configuration management (see Chapter 25).

## Slide 169: Hazard analysis
Hazard analysis involves identifying hazards and their root causes.
There should be clear traceability from identified hazards through their analysis to the actions taken during the process to ensure that these hazards have been covered.
A hazard log may be used to track hazards throughout the process.

## Slide 170: A simplified hazard log entry
Hazard Log Page 4: Printed 20.02.2012 |  |  |  |  |  | 
System: Insulin Pump System Safety Engineer: James Brown |  |  |  | File: InsulinPump/Safety/HazardLog Log version: 1/3 |  | 
Identified Hazard | Insulin overdose delivered to patient |  |  |  |  | 
Identified by | Jane Williams |  |  |  |  | 
Criticality class | 1 |  |  |  |  | 
Identified risk | High |  |  |  |  | 
Fault tree identified | YES | Date | 24.01.07 |  | Location | Hazard Log, Page 5
Fault tree creators | Jane Williams and Bill Smith |  |  |  |  | 
Fault tree checked | YES | Date | 28.01.07 |  | Checker | James Brown

## Slide 171: Hazard log (2)
System safety design requirements |  |  |  |  |  | 
1. The system shall include self-testing software that will test the sensor system, the clock, and the insulin delivery system. |  |  |  |  |  | 
2. The self-checking software shall be executed once per minute. |  |  |  |  |  | 
3. In the event of the self-checking software discovering a fault in any of the system components, an audible warning shall be issued and the pump display shall indicate the name of the component where the fault has been discovered. The delivery of insulin shall be suspended. |  |  |  |  |  | 
4. The system shall incorporate an override system that allows the system user to modify the computed dose of insulin that is to be delivered by the system. |  |  |  |  |  | 
5. The amount of override shall be no greater than a pre-set value (maxOverride), which is set when the system is configured by medical staff. |  |  |  |  |  | 

## Slide 172: Safety reviews
Driven by the hazard register.
For each identified hazrd, the review team should assess the system and judge whether or not the system can cope with that hazard in a safe way.

## Slide 173: Formal verification
Formal methods can be used when a mathematical specification of the system is produced.
They are the ultimate static verification technique that may be used at different stages in the development process:
  A formal specification may be developed and mathematically analyzed for consistency. This helps discover specification errors and omissions.
  Formal arguments that a program conforms to its mathematical specification may be developed. This is effective in discovering programming and design errors.

## Slide 174: Arguments for formal methods
Producing a mathematical specification requires a detailed analysis of the requirements and this is likely to uncover errors.
Concurrent systems can be analysed to discover race conditions that might lead to deadlock. Testing for such problems is very difficult.
They can detect implementation errors before testing when the program is analyzed alongside the specification.

## Slide 175: Arguments against formal methods
Require specialized notations that cannot be understood by domain experts.
Very expensive to develop a specification and even more expensive to show that a program meets that specification.
Proofs may contain errors.
It may be possible to reach the same level of confidence in a program more cheaply using other V & V techniques.

## Slide 176: Formal methods cannot guarantee safety
The specification may not reflect the real requirements of system users. Users rarely understand formal notations so they cannot directly read the formal specification to find errors and omissions.
The proof may contain errors. Program proofs are large and complex, so, like large and complex programs, they usually contain errors.
The proof may make incorrect assumptions about the way that the system is used. If the system is not used as anticipated, then the system’s behavior lies outside the scope of the proof.

## Slide 177: Model checking
Involves creating an extended finite state model of a system and, using a specialized system (a model checker), checking that model for errors.
The model checker explores all possible paths through the model and checks that a user-specified property is valid for each path.
Model checking is particularly valuable for verifying concurrent systems, which are hard to test.
Although model checking is computationally very expensive, it is now practical to use it in the verification of small to medium sized critical systems.

## Slide 178: Model checking

## Slide 179: Static program analysis
Static analysers are software tools for source text processing.
They parse the program text and try to discover potentially erroneous conditions and bring these to the attention of the V & V team.
They are very effective as an aid to inspections - they are a supplement to but not a replacement for inspections.

## Slide 180: Automated static analysis checks
Fault class | Static analysis check
Data faults | Variables used before initialization Variables declared but never used Variables assigned twice but never used between assignments Possible array bound violations Undeclared variables
Control faults | Unreachable code Unconditional branches into loops
Input/output faults | Variables output twice with no intervening assignment
Interface faults | Parameter-type mismatches Parameter number mismatches Non-usage of the results of functions Uncalled functions and procedures
Storage management faults | Unassigned pointers Pointer arithmetic Memory leaks

## Slide 181: Levels of static analysis
Characteristic error checking
  The static analyzer can check for patterns in the code that are characteristic of errors made by programmers using a particular language.
User-defined error checking
  Users of a programming language define error patterns, thus extending the types of error that can be detected. This allows specific rules that apply to a program to be checked.
Assertion checking
  Developers include formal assertions in their program and relationships that must hold. The static analyzer symbolically executes the code and highlights potential problems.

## Slide 182: Use of static analysis
Particularly valuable when a language such as C is used which has weak typing and hence many errors are undetected by the compiler.
Particularly valuable for security checking – the static analyzer can discover areas of vulnerability such as buffer overflows or unchecked inputs.
Static analysis is now routinely used in the development of many safety and security critical systems.

## Slide 183: Safety cases

## Slide 184: Safety and dependability cases
Safety and dependability cases are structured documents that set out detailed arguments and evidence that a required level of safety or dependability has been achieved.
They are normally required by regulators before a system can be certified for operational use. The regulator’s responsibility is to check that a system is as safe or dependable as is practical.
Regulators and developers work together and negotiate what needs to be included in a system safety/dependability case.

## Slide 185: The system safety case
A safety case is:
  A documented body of evidence that provides a convincing and valid argument that a system is adequately safe for a given application in a given environment.
Arguments in a safety case can be based on formal proof, design rationale, safety proofs, etc. Process factors may also be included.
A software safety case is usually part of a wider system safety case that takes hardware and operational issues into account.

## Slide 186: The contents of a software safety case
Chapter | Description
System description | An overview of the system and a description of its critical components.
Safety requirements | The safety requirements abstracted from the system requirements specification. Details of other relevant system requirements may also be included.
Hazard and risk analysis | Documents describing the hazards and risks that have been identified and the measures taken to reduce risk. Hazard analyses and hazard logs.
Design analysis | A set of structured arguments (see Section 15.5.1) that justify why the design is safe.
Verification and validation | A description of the V & V procedures used and, where appropriate, the test plans for the system. Summaries of the test results showing defects that have been detected and corrected. If formal methods have been used, a formal system specification and any analyses of that specification. Records of static analyses of the source code.

## Slide 187
Chapter | Description
Review reports | Records of all design and safety reviews.
Team competences | Evidence of the competence of all of the team involved in safety-related systems development and validation.
Process QA | Records of the quality assurance processes (see Chapter 24) carried out during system development.
Change management processes | Records of all changes proposed, actions taken and, where appropriate, justification of the safety of these changes. Information about configuration management procedures and configuration management logs.
Associated safety cases | References to other safety cases that may impact the safety case.

## Slide 188: Structured arguments
Safety cases should be based around structured arguments that present evidence to justify the assertions made in these arguments.
The argument justifies why a claim about system safety and security is justified by the available evidence.

## Slide 189: Structured arguments

## Slide 190: Insulin pump safety argument
Arguments are based on claims and evidence.
Insulin pump safety:
  Claim: The maximum single dose of insulin to be delivered (CurrentDose) will not exceed MaxDose.
  Evidence: Safety argument for insulin pump (discussed later)
  Evidence: Test data for insulin pump. The value of currentDose was correctly computed in 400 tests
  Evidence: Static analysis report for insulin pump software revealed no anomalies that affected the value of CurrentDose
  Argument: The evidence presented demonstrates that the maximum dose of insulin that can be computed = MaxDose.

## Slide 191: Structured safety arguments
Structured arguments that demonstrate that a system meets its safety obligations.
It is not necessary to demonstrate that the program works as intended; the aim is simply to demonstrate safety.
Generally based on a claim hierarchy.
  You start at the leaves of the hierarchy and demonstrate safety. This implies the higher-level claims are true.

## Slide 192: A safety claim hierarchy for the insulin pump

## Slide 193: Software safety arguments
Safety arguments are intended to show that the system cannot reach in unsafe state.
These are weaker than correctness arguments which must show that the system code conforms to its specification.
They are generally based on proof by contradiction
  Assume that an unsafe state can be reached;
  Show that this is contradicted by the program code.
A graphical model of the safety argument may be developed.

## Slide 194: Construction of a safety argument
Establish the safe exit conditions for a component or a program.
Starting from the END of the code, work backwards until you have identified all paths that lead to the exit of the code.
Assume that the exit condition is false.
Show that, for each path leading to the exit that the assignments made in that path contradict the assumption of an unsafe exit from the component.

## Slide 195: Insulin dose computation with safety checks
-- The insulin dose to be delivered is a function of blood sugar level,
-- the previous dose delivered and the time of delivery of the previous dose
currentDose = computeInsulin () ;
// Safety check—adjust currentDose if necessary.
// if statement 1
if (previousDose == 0)
{
if (currentDose > maxDose/2)
currentDose = maxDose/2 ;
}
else
if (currentDose > (previousDose * 2) )
currentDose = previousDose * 2 ;
// if statement 2
if ( currentDose < minimumDose )
currentDose = 0 ;
else if ( currentDose > maxDose )
currentDose = maxDose ;
administerInsulin (currentDose) ;

## Slide 196: Informal safety argument based on demonstrating contradictions

## Slide 197: Program paths
Neither branch of if-statement 2 is executed
  Can only happen if CurrentDose is >= minimumDose and <= maxDose.
then branch of if-statement 2 is executed
  currentDose = 0.
else branch of if-statement 2 is executed
  currentDose = maxDose.
In all cases, the post conditions contradict the unsafe condition that the dose administered is greater than maxDose.

## Slide 198: Key points
Safety-critical systems are systems whose failure can lead to human injury or death.
A hazard-driven approach is used to understand the safety requirements for safety-critical systems. You identify potential hazards and decompose these (using methods such as fault tree analysis) to discover their root causes. You then specify requirements to avoid or recover from these problems.
It is important to have a well-defined, certified process for safety-critical systems development. This should include the identification and monitoring of potential hazards.

## Slide 199: Key points
Static analysis is an approach to V & V that examines the source code of a system, looking for errors and anomalies. It allows all parts of a program to be checked, not just those parts that are exercised by system tests.
Model checking is a formal approach to static analysis that exhaustively checks all states in a system for potential errors.
Safety and dependability cases collect the evidence that demonstrates a system is safe and dependable. Safety cases are required when an external regulator must certify the system before it is used.

## Slide 200: Chapter 13 – Security Engineering

## Slide 201: Topics covered
Security and dependability
Security and organizations
Security requirements
Secure systems design
Security testing and assurance

## Slide 202: Security engineering
Tools, techniques and methods to support the development and maintenance of systems that can resist malicious attacks that are intended to damage a computer-based system or its data.
A sub-field of the broader field of computer security.

## Slide 203: Security dimensions
Confidentiality
  Information in a system may be disclosed or made accessible to people or programs that are not authorized to have access to that information.
Integrity
  Information in a system may be damaged or corrupted making it unusual or unreliable.
Availability
  Access to a system or its data that is normally available may not be possible.

## Slide 204: Security levels
Infrastructure security, which is concerned with maintaining the security of all systems and networks that provide an infrastructure and a set of shared services to the organization.
Application security, which is concerned with the security of individual application systems or related groups of systems.
Operational security, which is concerned with the secure operation and use of the organization’s systems.

## Slide 205: System layers where security may be compromised

## Slide 206: Application/infrastructure security
Application security is a software engineering problem where the system is designed to resist attacks.
Infrastructure security is a systems management problem where the infrastructure is configured to resist attacks.
The focus of this chapter is application security rather than infrastructure security.

## Slide 207: System security management
User and permission management
  Adding and removing users from the system and setting up appropriate permissions for users
Software deployment and maintenance
  Installing application software and middleware and configuring these systems so that vulnerabilities are avoided.
Attack monitoring, detection and recovery
  Monitoring the system for unauthorized access, design strategies for resisting attacks and develop backup and recovery strategies.

## Slide 208: Operational security
Primarily a human and social issue
Concerned with ensuring the people do not take actions that may compromise system security
  E.g. Tell others passwords, leave computers logged on
Users sometimes take insecure actions to make it easier for them to do their jobs
There is therefore a trade-off between system security and system effectiveness.

## Slide 209: Security and dependability

## Slide 210: Security
The security of a system is a system property that reflects the system’s ability to protect itself from accidental or deliberate external attack.
Security is essential as most systems are networked so that external access to the system through the Internet is possible.
Security is an essential pre-requisite for availability, reliability and safety.

## Slide 211: Fundamental security
If a system is a networked system and is insecure then statements about its reliability and its safety are unreliable.
These statements depend on the executing system and the developed system being the same. However, intrusion can change the executing system and/or its data.
Therefore, the reliability and safety assurance is no longer valid.

## Slide 212: Security terminology
Term | Definition
Asset | Something of value which has to be protected. The asset may be the software system itself or data used by that system.
Attack | An exploitation of a system’s vulnerability. Generally, this is from outside the system and is a deliberate attempt to cause some damage.
Control | A protective measure that reduces a system’s vulnerability. Encryption is an example of a control that reduces a vulnerability of a weak access control system
Exposure | Possible loss or harm to a computing system. This can be loss or damage to data, or can be a loss of time and effort if recovery is necessary after a security breach.
Threat | Circumstances that have potential to cause loss or harm. You can think of these as a system vulnerability that is subjected to an attack.
Vulnerability | A weakness in a computer-based system that may be exploited to cause loss or harm.

## Slide 213: Examples of security terminology (Mentcare)
Term | Example
Asset | The records of each patient that is receiving or has received treatment.
Exposure | Potential financial loss from future patients who do not seek treatment because they do not trust the clinic to maintain their data. Financial loss from legal action by the sports star. Loss of reputation.
Vulnerability | A weak password system which makes it easy for users to set guessable passwords. User ids that are the same as names.
Attack | An impersonation of an authorized user.
Threat | An unauthorized user will gain access to the system by guessing the credentials (login name and password) of an authorized user.
Control | A password checking system that disallows user passwords that are proper names or words that are normally included in a dictionary.

## Slide 214: Threat types
Interception threats that allow an attacker to gain access to an asset.
  A possible threat to the Mentcare system might be a situation where an attacker gains access to the records of an individual patient.
Interruption threats that allow an attacker to make part of the system unavailable.
  A possible threat might be a denial of service attack on a system database server so that database connections become impossible.

## Slide 215: Threat types
Modification threats that allow an attacker to tamper with a system asset.
  In the Mentcare system, a modification threat would be where an attacker alters or destroys a patient record.
Fabrication threats that allow an attacker to insert false information into a system.
  This is perhaps not a credible threat in the Mentcare system but would be a threat in a banking system, where false transactions might be added to the system that transfer money to the perpetrator’s bank account.

## Slide 216: Security assurance
Vulnerability avoidance
  The system is designed so that vulnerabilities do not occur. For example, if there is no external network connection then external attack is impossible
Attack detection and elimination
  The system is designed so that attacks on vulnerabilities are detected and neutralised before they result in an exposure. For example, virus checkers find and remove viruses before they infect a system
Exposure limitation and recovery
  The system is designed so that the adverse consequences of a successful attack are minimised. For example, a backup policy allows damaged information to be restored

## Slide 217: Security and dependability
Security and reliability
  If a system is attacked and the system or its data are corrupted as a consequence of that attack, then this may induce system failures that compromise the reliability of the system.
Security and availability
  A common attack on a web-based system is a denial of service attack, where a web server is flooded with service requests from a range of different sources. The aim of this attack is to make the system unavailable.

## Slide 218: Security and dependability
Security and safety
  An attack that corrupts the system or its data means that assumptions about safety may not hold. Safety checks rely on analysing the source code of safety critical software and assume the executing code is a completely accurate translation of that source code. If this is not the case, safety-related failures may be induced and the safety case made for the software is invalid.
Security and resilience
  Resilience is a system characteristic that reflects its ability to resist and recover from damaging events. The most probable damaging event on networked software systems is a cyberattack of some kind so most of the work now done in resilience is aimed at deterring, detecting and recovering from such attacks.

## Slide 219: Security and organizations

## Slide 220: Security is a business issue
Security is expensive and it is important that security decisions are made in a cost-effective way
  There is no point in spending more than the value of an asset to keep that asset secure.
Organizations use a risk-based approach to support security decision making and should have a defined security policy based on security risk analysis
Security risk analysis is a business rather than a technical process

## Slide 221: Organizational security policies
Security policies should set out general information access strategies that should apply across the organization.
The point of security policies is to inform everyone in an organization about security so these should not be long and detailed technical documents.
From a security engineering perspective, the security policy defines, in broad terms, the security goals of the organization.
The security engineering process is concerned with implementing these goals.

## Slide 222: Security policies
The assets that must be protected
  It is not cost-effective to apply stringent security procedures to all organizational assets. Many assets are not confidential and can be made freely available.
The level of protection that is required for different types of asset
  For sensitive personal information, a high level of security is required; for other information, the consequences of loss may be minor so a lower level of security is adequate.

## Slide 223: Security policies
The responsibilities of individual users, managers and the organization
  The security policy should set out what is expected of users e.g. strong passwords, log out of computers, office security, etc.
Existing security procedures and technologies that should be maintained
  For reasons of practicality and cost, it may be essential to continue to use existing approaches to security even where these have known limitations.

## Slide 224: Security risk assessment and management
Risk assessment and management is concerned with assessing the possible losses that might ensue from attacks on the system and balancing these losses against the costs of security procedures that may reduce these losses.
Risk management should be driven by an organisational security policy.
Risk management involves
  Preliminary risk assessment
  Life cycle risk assessment
  Operational risk assessment

## Slide 225: Preliminary risk assessment
The aim of this initial risk assessment is to identify generic risks that are applicable to the system and to decide if an adequate level of security can be achieved at a reasonable cost.
The risk assessment should focus on the identification and analysis of high-level risks to the system.
The outcomes of the risk assessment process are used to help identify security requirements.

## Slide 226: Design risk assessment
This risk assessment takes place during the system development life cycle and is informed by the technical system design and implementation decisions.
The results of the assessment may lead to changes to the security requirements and the addition of new requirements.
Known and potential vulnerabilities are identified, and this knowledge is used to inform decision making about the system functionality and how it is to be implemented, tested, and deployed.

## Slide 227: Operational risk assessment
This risk assessment process focuses on the use of the system and the possible risks that can arise from human behavior.
Operational risk assessment should continue after a system has been installed to take account of how the system is used.
Organizational changes may mean that the system is used in different ways from those originally planned. These changes lead to new security requirements that have to be implemented as the system evolves.

## Slide 228: Security requirements

## Slide 229: Security specification
Security specification has something in common with safety requirements specification – in both cases, your concern is to avoid something bad happening.
Four major differences
  Safety problems are accidental – the software is not operating in a hostile environment. In security, you must assume that attackers have knowledge of system weaknesses
  When safety failures occur, you can look for the root cause or weakness that led to the failure. When failure results from a deliberate attack, the attacker may conceal the cause of the failure.
  Shutting down a system can avoid a safety-related failure. Causing a shut down may be the aim of an attack.
  Safety-related events are not generated from an intelligent adversary. An attacker can probe defenses over time to discover weaknesses.

## Slide 230: Types of security requirement
Identification requirements.
Authentication requirements.
Authorisation requirements.
Immunity requirements.
Integrity requirements.
Intrusion detection requirements.
Non-repudiation requirements.
Privacy requirements.
Security auditing requirements.
System maintenance security requirements.

## Slide 231: Security requirement classification
Risk avoidance requirements set out the risks that should be avoided by designing the system so that these risks simply cannot arise.
Risk detection requirements define mechanisms that identify the risk if it arises and neutralise the risk before losses occur.
Risk mitigation requirements set out how the system should be designed so that it can recover from and restore system assets after some loss has occurred.

## Slide 232: The preliminary risk assessment process for security requirements

## Slide 233: Security risk assessment
Asset identification
  Identify the key system assets (or services) that have to be protected.
Asset value assessment
  Estimate the value of the identified assets.
Exposure assessment
  Assess the potential losses associated with each asset.
Threat identification
  Identify the most probable threats to the system assets

## Slide 234: Security risk assessment
Attack assessment
  Decompose threats into possible attacks on the system and the ways that these may occur.
Control identification
  Propose the controls that may be put in place to protect an asset.
Feasibility assessment
  Assess the technical feasibility and cost of the controls.
Security requirements definition
  Define system security requirements. These can be infrastructure or application system requirements.

## Slide 235: Asset analysis in a preliminary risk assessment report for the Mentcare system
Asset | Value | Exposure
The information system | High. Required to support all clinical consultations. Potentially safety-critical. | High. Financial loss as clinics may have to be canceled. Costs of restoring system. Possible patient harm if treatment cannot be prescribed.
The patient database | High. Required to support all clinical consultations. Potentially safety-critical. | High. Financial loss as clinics may have to be canceled. Costs of restoring system. Possible patient harm if treatment cannot be prescribed.
An individual patient record | Normally low although may be high for specific high-profile patients. | Low direct losses but possible loss of reputation.

## Slide 236: Threat and control analysis in a preliminary risk assessment report
Threat | Probability | Control | Feasibility
An unauthorized user gains access as system manager and makes system unavailable | Low | Only allow system management from specific locations that are physically secure. | Low cost of implementation but care must be taken with key distribution and to ensure that keys are available in the event of an emergency.
An unauthorized user gains access as system user and accesses confidential information | High | Require all users to authenticate themselves using a biometric mechanism. Log all changes to patient information to track system usage. | Technically feasible but high-cost solution. Possible user resistance. Simple and transparent to implement and also supports recovery.

## Slide 237: Security requirements for the Mentcare system
Patient information shall be downloaded at the start of a clinic session to a secure area on the system client that is used by clinical staff.
All patient information on the system client shall be encrypted.
Patient information shall be uploaded to the database after a clinic session has finished and deleted from the client computer.
A log on a separate computer from the database server must be maintained of all changes made to the system database.

## Slide 238: Misuse cases
Misuse cases are instances of threats to a system
Interception threats
  Attacker gains access to an asset
Interruption threats
  Attacker makes part of a system unavailable
Modification threats
  A system asset if tampered with
Fabrication threats
  False information is added to a system

## Slide 239: Misuse cases

## Slide 240: Mentcare use case – Transfer data
Mentcare system: Transfer data | 
Actors | Medical receptionist, Patient records system (PRS)
Description | A receptionist may transfer data from the Mentcare system to a general patient record database that is maintained by a health authority. The information transferred may either be updated personal information (address, phone number, etc.) or a summary of the patient’s diagnosis and treatment.
Data | Patient’s personal information, treatment summary.
Stimulus | User command issued by medical receptionist.
Response | Confirmation that PRS has been updated.
Comments | The receptionist must have appropriate security permissions to access the patient information and the PRS.

## Slide 241: Mentcare misuse case: Intercept transfer
Mentcare system: Intercept transfer (Misuse case) | 
Actors | Medical receptionist, Patient records system (PRS), Attacker
Description | A receptionist transfers data from his or her PC to the Mentcare system on the server. An attacker intercepts the data transfer and takes a copy of that data.
Data (assets) | Patient’s personal information, treatment summary
Attacks | A network monitor is added to the system and packets from the receptionist to the server are intercepted. A spoof server is set up between the receptionist and the database server so that receptionist believes they are interacting with the real system.

## Slide 242: Misuse case: Intercept transfer
Mentcare system: Intercept transfer (Misuse case) | 
Mitigations | All networking equipment must be maintained in a locked room. Engineers accessing the equipment must be accredited. All data transfers between the client and server must be encrypted. Certificate-based client-server communication must be used
Requirements | All communications between the client and the server must use the Secure Socket Layer (SSL). The https protocol uses certificate based authentication and encryption.

## Slide 243: Secure systems design

## Slide 244: Secure systems design
Security should be designed into a system – it is very difficult to make an insecure system secure after it has been designed or implemented
Architectural design
  how do architectural design decisions affect the security of a system?
Good practice
  what is accepted good practice when designing secure systems?

## Slide 245: Design compromises
Adding security features to a system to enhance its security affects other attributes of the system
Performance
  Additional security checks slow down a system so its response time or throughput may be affected
Usability
  Security measures may require users to remember information or require additional interactions to complete a transaction. This makes the system less usable and can frustrate system users.

## Slide 246: Design risk assessment
Risk assessment while the system is being developed and after it has been deployed
More information is available - system platform, middleware and the system architecture and data organisation.
Vulnerabilities that arise from design choices may therefore be identified.

## Slide 247: Design and risk assessment

## Slide 248: Protection requirements
Protection requirements may be generated when knowledge of information representation and system distribution
Separating patient and treatment information limits the amount of information (personal patient data) that needs to be protected
Maintaining copies of records on a local client protects against denial of service attacks on the server
  But these may need to be encrypted

## Slide 249: Design risk assessment

## Slide 250: Design decisions from use of COTS
System users authenticated using a name/password combination.
The system architecture is client-server with clients accessing the system through a standard web browser.
Information is presented as an editable web form.

## Slide 251: Vulnerabilities associated with technology choices

## Slide 252: Security requirements
A password checker shall be made available and shall be run daily. Weak passwords shall be reported to system administrators.
Access to the system shall only be allowed by approved client computers.
All client computers shall have a single, approved web browser installed by system administrators.

## Slide 253: Architectural design
Two fundamental issues have to be considered when designing an architecture for security.
  Protection
    How should the system be organised so that critical assets can be protected against external attack?
  Distribution
    How should system assets be distributed so that the effects of a successful attack are minimized?
These are potentially conflicting
  If assets are distributed, then they are more expensive to protect. If assets are protected, then usability and performance requirements may be compromised.

## Slide 254: Protection
Platform-level protection
  Top-level controls on the platform on which a system runs.
Application-level protection
  Specific protection mechanisms built into the application itself e.g. additional password protection.
Record-level protection
  Protection that is invoked when access to specific information is requested
These lead to a layered protection architecture

## Slide 255: A layered protection architecture

## Slide 256: Distribution
Distributing assets means that attacks on one system do not necessarily lead to complete loss of system service
Each platform has separate protection features and may be different from other platforms so that they do not share a common vulnerability
Distribution is particularly important if the risk of denial of service attacks is high

## Slide 257: Distributed assets in an equity trading system

## Slide 258: Design guidelines for security engineering
Design guidelines encapsulate good practice in secure systems design
Design guidelines serve two purposes:
  They raise awareness of security issues in a software engineering team. Security is considered when design decisions are made.
  They can be used as the basis of a review checklist that is applied during the system validation process.
Design guidelines here are applicable during software specification and design

## Slide 259: Design guidelines for secure systems engineering
Security guidelines | 
Base security decisions on an explicit security policy | 
Avoid a single point of failure | 
Fail securely | 
Balance security and usability | 
Log user actions | 
Use redundancy and diversity to reduce risk | 
Specify the format of all system inputs | 
Compartmentalize your assets | 
Design for deployment | 
Design for recoverability | 

## Slide 260: Design guidelines 1-3
Base decisions on an explicit security policy
  Define a security policy for the organization that sets out the fundamental security requirements that should apply to all organizational systems.
Avoid a single point of failure
  Ensure that a security failure can only result when there is more than one failure in security procedures. For example, have password and question-based authentication.
Fail securely
  When systems fail, for whatever reason, ensure that sensitive information cannot be accessed by unauthorized users even although normal security procedures are unavailable.

## Slide 261: Design guidelines 4-6
Balance security and usability
  Try to avoid security procedures that make the system difficult to use. Sometimes you have to accept weaker security to make the system more usable.
Log user actions
  Maintain a log of user actions that can be analyzed to discover who did what. If users know about such a log, they are less likely to behave in an irresponsible way.
Use redundancy and diversity to reduce risk
  Keep multiple copies of data and use diverse infrastructure so that an infrastructure vulnerability cannot be the single point of failure.

## Slide 262: Design guidelines 7-10
Specify the format of all system inputs
  If input formats are known then you can check that all inputs are within range so that unexpected inputs don’t cause problems.
Compartmentalize your assets
  Organize the system so that assets are in separate areas and users only have access to the information that they need rather than all system information.
Design for deployment
  Design the system to avoid deployment problems
Design for recoverability
  Design the system to simplify recoverability after a successful attack.

## Slide 263: Secure systems programming

## Slide 264: Aspects of secure systems programming
Vulnerabilities are often language-specific.
  Array bound checking is automatic in languages like Java so this is not a vulnerability that can be exploited in Java programs.
  However, millions of programs are written in C and C++ as these allow for the development of more efficient software so simply avoiding the use of these languages is not a realistic option.
Security vulnerabilities are closely related to program reliability.
  Programs without array bound checking can crash so actions taken to improve program reliability can also improve system security.

## Slide 265: Dependable programming guidelines
Dependable programming guidelines 1. Limit the visibility of information in a program 2. Check all inputs for validity 3. Provide a handler for all exceptions 4. Minimize the use of error-prone constructs 5. Provide restart capabilities 6. Check array bounds 7. Include timeouts when calling external components 8. Name all constants that represent real-world values | 

## Slide 266: Security testing and assurance

## Slide 267: Security testing
Testing the extent to which the system can protect itself from external attacks.
Problems with security testing
  Security requirements are ‘shall not’ requirements i.e. they specify what should not happen. It is not usually possible to define security requirements as simple constraints that can be checked by the system.
  The people attacking a system are intelligent and look for vulnerabilities. They can experiment to discover weaknesses and loopholes in the system.

## Slide 268: Security validation
Experience-based testing
  The system is reviewed and analysed against the types of attack that are known to the validation team.
Penetration testing
  A team is established whose goal is to breach the security of the system by simulating attacks on the system.
Tool-based analysis
  Various security tools such as password checkers are used to analyse the system in operation.
Formal verification
  The system is verified against a formal security specification.

## Slide 269: Examples of entries in a security checklist
Security checklist
1. Do all files that are created in the application have appropriate access permissions? The wrong access permissions may lead to these files being accessed by unauthorized users.
2. Does the system automatically terminate user sessions after a period of inactivity? Sessions that are left active may allow unauthorized access through an unattended computer.
3. If the system is written in a programming language without array bound checking, are there situations where buffer overflow may be exploited? Buffer overflow may allow attackers to send code strings to the system and then execute them.
4. If passwords are set, does the system check that passwords are ‘strong’? Strong passwords consist of mixed letters, numbers, and punctuation, and are not normal dictionary entries. They are more difficult to break than simple passwords.
5. Are inputs from the system’s environment always checked against an input specification? Incorrect processing of badly formed inputs is a common cause of security vulnerabilities.

## Slide 270: Key points
Security engineering is concerned with how to develop systems that can resist malicious attacks
Security threats can be threats to confidentiality, integrity or availability of a system or its data
Security risk management is concerned with assessing possible losses from attacks and deriving security requirements to minimise losses
To specify security requirements, you should identify the assets that are to be protected and define how security techniques and technology should be used to protect these assets.

## Slide 271: Key points
Key issues when designing a secure systems architecture include organizing the system structure to protect key assets and distributing the system assets to minimize the losses from a successful attack.
Security design guidelines sensitize system designers to security issues that they may not have considered. They provide a basis for creating security review checklists.
Security validation is difficult because security requirements state what should not happen in a system, rather than what should. Furthermore, system attackers are intelligent and may have more time to probe for weaknesses than is available for security testing.

## Slide 272
Chapter 14 – Resilience Engineering

## Slide 273: Topics covered
Cybersecurity
Sociotechnical resilience
Resilient systems design

## Slide 274: Resilience
The resilience of a system is a judgment of how well that system can maintain the continuity of its critical services in the presence of disruptive events, such as equipment failure and cyberattacks.
Cyberattacks by malicious outsiders are perhaps the most serious threat faced by networked systems but resilience is also intended to cope with system failures and other disruptive events.

## Slide 275: Essential resilience ideas
The idea that some of the services offered by a system are critical services whose failure could have serious human, social or economic effects.
The idea that some events are disruptive and can affect the ability of a system to deliver its critical services.
The idea that resilience is a judgment – there are no resilience metrics and resilience cannot be measured. The resilience of a system can only be assessed by experts, who can examine the system and its operational processes.

## Slide 276: Resilience engineering assumptions
Resilience engineering assumes that it is impossible to avoid system failures and so is concerned with limiting the costs of these failures and recovering from them.
Resilience engineering assumes that good reliability engineering practices have been used to minimize the number of technical faults in a system.
It therefore places more emphasis on limiting the number of system failures that arise from external events such as operator errors or cyberattacks.

## Slide 277: Resilience activities
Recognition The system or its operators should recognise early indications of system failure.
Resistance If the symptoms of a problem or cyberattack are detected early, then resistance strategies may be used to reduce the probability that the system will fail.
Recovery If a failure occurs, the recovery activity ensures that critical system services are restored quickly so that system users are not badly affected by failure.
Reinstatement In this final activity, all of the system services are restored and normal system operation can continue.

## Slide 278: Resistance
Resistance strategies may focus on isolating critical parts of the system so that they are unaffected by problems elsewhere.
Resistance includes proactive resistance where defences are included in a system to trap problems and reactive resistance where actions are taken when a problem is discovered.

## Slide 279: Resilience activities

## Slide 280: Cybersecurity

## Slide 281: Cybersecurity
Cybercrime is the illegal use of networked systems and is one of the most serious problems facing our society.
Cybersecurity is a broader topic than system security engineering
  Cybersecurity is a sociotchnical issue covering all aspects of ensuring the protection of citizens, businesses and critical infrastructures from threats that arise from their use of computers and the Internet.
Cybersecurity is concerned with all of an organization’s IT assets from networks through to application systems.

## Slide 282: Factors contributing to cybersecurity failure
organizational ignorance of the seriousness of the problem,
poor design and lax application of security procedures,
human carelessness,
inappropriate trade-offs between usability and security.

## Slide 283: Cybersecurity threats
Threats to the confidentiality of assets Data is not damaged but it is made available to people who should not have access to it.
Threats to the integrity of assets These are threats where systems or data are damaged in some way by a cyberattack.
Threats to the availability of assets These are threats that aim to deny use of assets by authorized users.

## Slide 284: Examples of controls
Authentication, where users of a system have to show that they are authorized to access the system
Encryption, where data is algorithmically scrambled so that an unauthorized reader cannot access the information.
Firewalls, where incoming network packets are examined then accepted or rejected according to a set of organizational rules.
  Firewalls can be used to ensure that only traffic from trusted sources is passed from the external Internet into the local organizational network.

## Slide 285: Redundancy and diversity
Copies of data and software should be maintained on separate computer systems.
  This supports recovery after a successful cyberattack. (recovery and reinstatement)
Multi-stage diverse authentication can protect against password attacks.
  This is a resistance measure
Critical servers may be over-provisioned i.e. they may be more powerful than is required to handle their expected load. Attacks can be resisted without serious service degradation.

## Slide 286: Cyber-resilience planning

## Slide 287: Cyber resilience planning
Asset classification
  The organization’s hardware, software and human assets are examined and classified depending on how essential they are to normal operations.
Threat identification
  For each of the assets (or, at least the critical and important assets), you should identify and classify threats to that asset.
Threat recognition
  For each threat or, sometimes asset/threat pair, you should identify how an attack based on that threat might be recognised.

## Slide 288: Cyber resilience planning
Threat resistance
  For each threat or asset/threat pair, you should identify possible resistance strategies. These may be either embedded in the system (technical strategies) or may rely on operational procedures.
Asset recovery
  For each critical asset or asset/threat pair, you should work out how that asset could be recovered in the event of a successful cyberattack.
Asset reinstatement
    This is a more general process of asset recovery where you define procedures to bring the system back into normal operation.

## Slide 289: Sociotechnical resilience

## Slide 290: Sociotechnical resilience
Resilience engineering is concerned with adverse external events that can lead to system failure.
To design a resilient system, you have to think about sociotechnical systems design and not exclusively focus on software.
Dealing with these events is often easier and more effective in the broader sociotechnical system.

## Slide 291: Mentcare example
Cyberattack may aim to steal data, gaining access using a legitimate user’s credentials
Technical solution may be to use more complex authentication procedures.
These irritate users and may reduce security as users leave systems unattended without logging out.
A better strategy may be to introduce organizational policies and procedures that emphasise the importance of not sharing login credentials and that tell users about easy ways to create and maintain strong passwords.

## Slide 292: Nested technical and sociotechnical systems

## Slide 293: Failure hierarchy
A failure in system S1 may be trapped in the broader sociotechnical system ST1 through operator actions
Organizational damage is therefore limited
If the failure in S1 leads to a failure in ST1, then it is up to managers in the broader organization to deal with that failure.

## Slide 294: Characteristics of resilient organizations

## Slide 295: Organizational resilience
There are four characteristics that reflect the resilience of an organization
  Responsiveness, monitoring, anticipation, learning
The ability to respond
  Organizations have to be able to adapt their processes and procedures in response to risks. These risks may be anticipated risks or may be detected threats to the organization and its systems.
The ability to monitor
  Organizations should monitor both their internal operations and their external environment for threats before they arise.

## Slide 296: Organizational resilience
The ability to anticipate
  A resilient organization should not simply focus on its current operations but should anticipate possible future events and changes that may affect its operations and resilience.
The ability to learn
  Organizational resilience can be improved by learning from experience. It is particularly important to learn from successful responses to adverse events such as the effective resistance of a cyberattack. Learning from success allows

## Slide 297: Human error
People inevitably make mistakes (human errors) that sometimes lead to serious system failures.
There are two ways to consider human error
  The person approach. Errors are considered to be the responsibility of the individual and ‘unsafe acts’ (such as an operator failing to engage a safety barrier) are a consequence of individual carelessness or reckless behaviour.
  The systems approach. The basic assumption is that people are fallible and will make mistakes. People make mistakes because they are under pressure from high workloads, poor training or because of inappropriate system design.

## Slide 298: Systems approach
Systems engineers should assume that human errors will occur during system operation.
To improve the resilience of a system, designers have to think about the defences and barriers to human error that could be part of a system.
Can these barriers should be built into the technical components of the system (technical barriers)? If not, they could be part of the processes, procedures and guidelines for using the system (sociotechnical barriers).

## Slide 299: Defensive layers

## Slide 300: Defensive layers
You should use redundancy and diversity to create a set of defensive layers, where each layer uses a different approach to deter attackers or trap technical/human failures.
ATC system examples
  Conflict alert system
  Formalized recording procedures
  Collaborative checking

## Slide 301: Reason’s Swiss Cheese Model

## Slide 302: Swiss Cheese model
Defensive layers have vulnerabilities
  They are like slices of Swiss cheese with holes in the layer corresponding to these vulnerabilities.
Vulnerabilities are dynamic
  The ‘holes’ are not always in the same place and the size of the holes may vary depending on the operating conditions.
System failures occur when the holes line up and all of the defenses fail.

## Slide 303: Increasing system resilience
Reduce the probability of the occurrence of an external event that might trigger system failures.
Increase the number of defensive layers.
  The more layers that you have in a system, the less likely it is that the holes will line up and a system failure occur.
Design a system so that diverse types of barriers are included.
  The ‘holes’ will probably be in different places and so there is less chance of the holes lining up and failing to trap an error.
Minimize the number of latent conditions in a system.
  This means reducing the number and size of system ‘holes’.

## Slide 304: Operational and management processes
All software systems have associated operational processes that reflect the assumptions of the designers about how these systems will be used.
For example, in an imaging system in a hospital, the operator may have the responsibility of checking the quality of the images immediately after these have been processed.
This allows the imaging procedure to be repeated if there is a problem.

## Slide 305: Operational processes
Operational processes are the processes that are involved in using the system for its defined purpose.
For new systems, these operational processes have to be defined and documented during the system development process.
Operators may have to be trained and other work processes adapted to make effective use of the new system.

## Slide 306: Personal and Enterprise IT processes
For personal systems, the designers may describe the expected use of the system but have no control over how users will actually behave.
For enterprise IT systems, however, there may be training for users to teach them how to use the system.
Although user behaviour cannot be controlled, it is reasonable to expect that they will normally follow the defined process.

## Slide 307: Process design
Operational and management processes are an important defense mechanism and, in designing a process, you need to find a balance between efficient operation and problem management.
Process improvement focuses on identifying and codifying good practice and developing software to support this.
If process improvement focuses on efficiency, then this can make it more difficult to deal with problems when these arise.

## Slide 308: Efficiency and resilience
Efficient process operation | Problem management
Process optimization and control | Process flexibility and adaptability
Information hiding and security | Information sharing and visibility
Automation to reduce operator workload with fewer operators and managers | Manual processes and spare operator/manager capacity to deal with problems
Role specialization | Role sharing

## Slide 309: Coping with failures
What seems to be ‘inefficient’ practice often arises because people maintain redundant information or share information because they know this makes it easier to deal with problems when things go wrong.
When things go wrong, operators and system managers can often recover the situation although this may sometimes mean that they have to break rules and ‘work around’ the defined process.
You should therefore design operational processes to be flexible and adaptable.

## Slide 310: Information provision and management
To make a process more efficient, it may make sense to present operators with the information that they need, when they need it.
If operators are only presented with information that the process designer thinks that they ‘need to know’ then they may be unable to detect problems that do not directly affect their immediate tasks.
When things go wrong, the system operators do not have a broad picture of what is happening in the system, so it is more difficult for them to formulate strategies for dealing with problems.

## Slide 311: Process automation
Process automation can have both positive and negative effects on system resilience.
If the automated system works properly, it can detect problems, invoke cyberattack resistance if necessary and start automated recovery procedures.
However, if the problem can’t be handled by the automated system, there are fewer people available to tackle the problem and the system may have been damaged by the process automation doing the wrong thing.

## Slide 312: Disadvantages of process automation
Automated management systems may go wrong and take incorrect actions. As problems develop, the system may take unexpected actions that make the situation worse and which cannot be understood by the system managers.
Problem solving is a collaborative process. If fewer managers are available, it is likely to take longer to work out a strategy to recover from a problem or cyberattack.

## Slide 313: Resilient systems design

## Slide 314: Resilient systems design
Identifying critical services and assets
  Critical services and assets are those elements of the system that allow a system to fulfill its primary purpose.
  For example, the critical services in a system that handles ambulance dispatch are those concerned with taking calls and dispatching ambulances.
Designing system components that support problem recognition, resistance, recovery and reinstatement
  For example, in an ambulance dispatch system, a watchdog timer may be included to detect if the system is not responding to events.

## Slide 315: Survivable systems analysis
System understanding
  For an existing or proposed system, review the goals of the system (sometimes called the mission objectives), the system requirements and the system architecture.
Critical service identification
  The services that must always be maintained and the components that are required to maintain these services are identified.

## Slide 316: Survivable systems analysis
Attack simulation
  Scenarios or use cases for possible attacks are identified along with the system components that would be affected by these attacks.
Survivability analysis
  Components that are both essential and compromisable by an attack are identified and survivability strategies based on resistance, recognition and recovery are identified.

## Slide 317: Stages in survivability analysis

## Slide 318: Problems for business systems
The fundamental problem with this approach to survivability analysis is that its starting point is the requirements and architecture documentation for a system.
However for business systems:
  It is not explicitly related to the business requirements for resilience. I believe that these are a more appropriate starting point than technical system requirements.
  It assumes that there is a detailed requirements statement for a system. In fact, resilience may have to be ‘retrofitted’ to a system where there is no complete or up-to-date requirements document.

## Slide 319: Resilience engineering

## Slide 320: Streams of work in resilience engineering
Identify business resilience requirements
Plan how to reinstate systems to their normal operating state
Identify system failures and cyberattacks that can compromise a system
Plan how to recover critical services quickly after damage or a cyberattack
Test all aspects of resilience planning

## Slide 321: Maintaining critical service availability
To maintain availability, you need to know:
  the system services that are the most critical for a business,
  the minimal quality of service that must be maintained,
  how these services might be compromised,
  how these services can be protected,
  how you can recover quickly if the services become unavailable.
Critical assets are identified during service analysis.
  Assets may be hardware, software, data or people.

## Slide 322: Mentcare system resilience
The Mentcare system is a system used to support clinicians treating patients that suffer from mental health problems.
It provides patient information and records of consultations with doctors and nurses.
It includes checks that can flag patients who may be dangerous or suicidal.
Based on a client-server architecture.

## Slide 323: Client-server architecture (Mentcare)

## Slide 324: Critical Mentcare services
An information service that provides information about a patient’s current diagnosis and treatment plan.
A warning service that highlights patients that could pose a danger to others or to themselves.
Availability of the complete patient record is NOT a critical service as routine patient information is not normally required during consultations.

## Slide 325: Assets required for normal service operation
The patient record database that maintains all patient information.
A database server that provides access to the database for local client computers.
A network for client/server communication.
Local laptop or desktop computers used by clinicians to access patient information.
A set of rules to identify patients who are potentially dangerous and which can flag patient records. Client software that highlights dangerous patients to system users.

## Slide 326: Adverse events
Unavailability of the database server either through a system failure, a network failure or a denial of service cyberattack
Deliberate or accidental corruption of the patient record database or the rules that define what is meant by a ‘dangerous patient’
Infection of client computers with malware
Access to client computers by unauthorized people who gain access to patient records

## Slide 327: Recognition and resistance strategies
Event | Recognition | Resistance
Server unavailability | 1. Watchdog timer on client that times out if no response to client access 2. Text messages from system managers to clinical users | 1. Design system architecture to maintain local copies of critical information 2. Provide peer-to-peer search across clients for patient data 3. Provide staff with smart phones that can be used to access the network in the event of server failure 4. Provide backup server
Patient database corruption | 1. Record level cryptographic checksums 2. Regular auto-checking of database integrity 3. Reporting system for incorrect information | 1. Replayable transaction log to update database backup with recent transactions 2. Maintenance of local copies of patient information and software to restore database from local copies and backups
Malware infection of client computers | 1. Reporting system so that computer users can report unusual behaviour. 2. Automated malware checks on startup. | 1. Security awareness workshops for all system users 2. Disabling of USB ports on client computers 3. Automated system setup for new clients 4. Support access to system from mobile devices 5. Installation of security software
Unauthorized access to patient information | 1. Warning text messages from users about possible intruders 2. Log analysis for unusual activity | 1. Multi-level system authentication process 2. Disabling of USB ports on client computers 3. Access logging and real-time log analysis 4. Security awareness workshops for all system users

## Slide 328: Mentcare system resilience

## Slide 329: Architecture for resilience
Summary patient records that are maintained on local client computers.
  The local computers can communicate directly with each other and exchange information using either the system network or using an ad hoc network created using mobile phones. If the database is unavailable, doctors and nurses can still access essential patient information.
A backup server to allow for main server failure.
  This server is responsible for taking regular snapshots of the database as backups. In the event of the failure of the main server, it can also act as the main server for the whole system.

## Slide 330: Architecture for resilience
Database integrity checking and recovery software.
  Integrity checking runs as a background task checking for signs of database corruption. If corruption is discovered, it can automatically initiate the recovery of some or all of the data from backups. The transaction log allows these backups to be updated with details of recent changes

## Slide 331: Critical service maintenance
By downloading information to the client at the start of a clinic session, the consultation can continue without server access.
  Only the information about the patients who are scheduled to attend consultations that day needs to be downloaded.
The service that provides a warning to staff of patients that may be dangerous can be implemented using this approach.
  The records of possibly patients who may harm themselves or others are identified before the download process. When clinical staff access these records, the software can highlight them to indicate that this is a patient that requires special care.

## Slide 332: Risks to confidentiality
To minimize risks to confidentiality that arise from multiple copies of information on laptops:
  Only download the summary records of patients who are scheduled to attend a clinic. This limits the numbers of records that could be compromised.
  Encrypt the disk on local client computers. An attacker who does not have the encryption key cannot read the disk if they gain access to the computer.
  Securely delete the downloaded information at the end of a clinic session. This further reduces the chances of an attacker gaining access to confidential information.
  Ensure that all network transactions are encrypted. If an attacker intercepts these transactions, they cannot get access to the information.

## Slide 333: Key points
Resilience is a judgment of how well a system can maintain the continuity of its critical services in the presence of disruptive events.
Resilience should be based on the 4 R’s model – recognition, resistance, recovery and reinstatement.
Resilience planning should be based on the assumption of cyberattacks by malicious insiders and outsiders and that some of these attacks will be successful.
Systems should be designed with defensive layers of different types. These layers trap human and technical failures and help resist cyberattacks.

## Slide 334: Key points
To allow system operators and managers to cope with problems, processes should be flexible and adaptable. Process automation can make it more difficult for people to cope with problems.
Business resilience requirements should be the starting point for designing systems for resilience. To achieve system resilience, you have to focus on recognition and recovery from problems, recovery of critical services and assets and reinstatement of the system.
An important part of design for resilience is identifying critical services. Systems should be designed so that these services are protected and, in the event of failure, recovered as quickly as possible.